Tntnet configuration-reference
Author: Tommi Mäkitalo
Date: 2010-06-21
For Tntnet version 2.0

# AccessLog
## Syntax
AccessLog filename
## Description
If a filename is given, a logentry for each request is written to the file. The format of the file is the same as in other common web servers.
## Example
AccessLog /var/log/tntnet/access.log
# BufferSize
## Syntax
BufferSize bytes
## Description
Specifies the number of bytes sent in a single system-call. This does not limit anything in application-level. It does not affect e.g. savepoints or exception-handling. Component-output is collected completely and then passed in chunks of BufferSize bytes to the operating system.
The default value for this is 16384.
## Example
BufferSize 32768
# CompLifetime
## Syntax
CompLifetime seconds
## Description
Components are instatiated when needed and reused. After the time specified here the instances are deleted. This defaults to 600 seconds.
## Example
CompLifetime 120
# CompPath
## Syntax
CompPath directory
## Description
CompPath specifies, where tntnet should search for webapplications. Tntnet searches first in the current directory and then in each directory, you specify here, until a library is found. You can repeat the directive as many times as desired to add more entries. If it is not found, the next MapUrl-entry is tried.
## Example
CompPath /usr/local/lib/tntnet
CompPath /usr/local/share/tntnet
# Chroot
## Syntax
Chroot directory
## Description
Does a chroot(2)-system call on startup, which locks the process into the directory at system-level.
## Example
Chroot /var/tntnet
# Daemon
## Syntax
Daemon 0|1
## Description
If this flag is set to 1, Tntnet forks at startup and terminates the parent-process on successful initialization.
## Example
Daemon 1
# DefaultContentType
## Syntax
DefaultContentType contenttype
## Description
Sets the default content type. This content type is set in the http header, if the component does not set it. The default is “text/html; charset=UTF-8”
## Example
DefaultContentType "text/html; charset=ISO8859-1"
# Dir
## Syntax
Dir directory
## Description
Changes the current working directory of the process on startup.
## Example
Dir /var/tntnet
# EnableCompression
## Syntax
EnableCompression yes|no
## Description
Specifies, if Tntnet should use gzip-compression at http-level. By default Tntnet use compression.
A http-client like a web browser can send a header “Accept-Encoding”, to tell Tntnet, that it would accept compressed data. Tntnet then can decide, if it use compression. When the body is complete, Tntnet tries to compress the body. If the data can be compressed by more than 10%, Tntnet sends this compressed data. With this flag, this feature can be turned off.
Compression slows down processing but reduces the network-load. Normally the size of html-pages can be compressed by about 70%, while Tntnet slows down by up to 30%.
## Example
EnableCompression no
# Group
## Syntax
Group unix-group
## Description
Changes the group under which tntnet answers requests.
## Example
Group tntnet-group
# include
## Syntax
include filemask
## Description
Reads additional settings from the specified files. filemask might contain glob-characters, so that multiple files might be read. The order is not specified.
## Example
include /etc/tntnet.d/*.conf
# KeepAliveTimeout
## Syntax
KeepAliveTimeout milliseconds
## Description
Sets the timeout for keep-alive requests. Tntnet tries to do keep-alive-requests wherever possible. This has the effect, that tntnet can receive multiple requests within a single tcp-connection. The connection times out after KeepAliveTimeout milliseconds. The timeout defaults to 15000ms.
## Example
KeepAliveTimeout 300000
sets the keep-alive-timeout to 5 minutes.
# KeepAliveMax
## Syntax
KeepAliveMax number
## Description
Sets the maximum number of request per tcp-connection. This defaults to 100.
## Example
KeepAliveMax 10
# Listen
## Syntax
Listen ip [port]
## Description
Specifies, on which address tntnet waits for connections. There can be more than one Listen-directives, in which case tntnet waits on every address. If there is no Listen-directive tntnet listens on 0.0.0.0 port 80.
ip might also be a hostname.
## Example
Listen 127.0.0.1 8000
Listens on localhost on port 8000.
# ListenRetry
## Syntax
ListenRetry number
## Description
On startup Tntnet calls listen on the specified port. When the systemcall returns with an error, Tntnet tries again and fails after the specified number of attempts. The default number is 5.
## Example
ListenRetry 10
Retries 10 times
# ListenBacklog
## Syntax
ListenBacklog number
## Description
The system-call listen needs a parameter backlog, which specifies, how many pending connections the operating-system should queue before it starts to ignore new request. The value is configurable here.
The default value is 16.
## Example
ListenBacklog 64
Changes the backlog-queue to 64.
# Load
## Syntax
Load webapplication
## Description
Load specifies, which webapplications are preloaded on startup. Normally webapplications are loaded as needed. The disadvantage is, that there is no way to check on startup, if a application is loadable at all. With this directive startup fails, if the application is not loadable.
## Example
Load myapp
# MapUrl
## Syntax
MapUrl url component-identifier [ path-info { additional-arguments } ]
## Description
Tells tntnet, which component should be called, when it receives a http-request. url is a regular expression, which is tried against the request-url. If it matches, the component-identifier is evaluated. component-idetifier may contain backreferences to the url. By default the url is passed as path-info to the component, but this can be changed with a third parameter. Additional parameters can be passed to the component and accessed through tnt::httpRequest::getArgs().
This variable can occur more than once and they are tried in the order they are found in the configurationfile, until the regular expression matches and the component does not return tnt::DECLINED. If no MapUrl-directive is found, http-error 404 (not found) is sent.
## Example
# maps html-pages to components in myapp.so; e.g. /foo.html calls foo@myapp
MapUrl /([^/.]+)\.html	$1@myapp
# maps jpeg-urls to myapp; e.g. /foo.jpeg calls foo_jpg@myapp
MapUrl /([^/.]+)\.jpeg	$1_jpg@myapp
# maps /foo/bar.html to bar@foo
MapUrl /([^/.]+)/([^/.]\.html	$2@$1
# MaxUrlMapCache
## Syntax
MaxUrlMapCache size
## Description
As described in MapUrl urls are mapped to components with regular expressions. This is a quite expensive operation, while the number of different urls used in a typical web application is small. Therefore Tntnet has a simple cache, which stores mappings to prevent the need to process the same regular expression multiple times. The size of this cache is limited. After the size is exceeded the cache is simply cleared. This clearing is logged with the message “clear url-map-cache”. If you have a application whit many different urls and you often see this warning-message, you might want to increase the cache.
The default value is 8192.
## Example
MaxUrlMapCache 32768
# MaxRequestSize
## Syntax
MaxRequestSize number
## Description
This directive limits the size of the request. After number Bytes the connection is just closed.
This prevents deniel-of-service-attacks through long requests. Every request is read into memory, so it must fit into it.
Bear in mind, that if you use file-upload-fields a request might be larger than just a few bytes.
The value defaults to 0, which means, that there is no limit at all.
## Example
MaxRequestSize 65536
# MaxUrlMapCache
## Syntax
MaxUrlMapCache number
## Description
Tntnet has a cache, which stores results from the MapUrl setting. Since processing regular expressions as used in MapUrl does take time and often only a few distinct urls are processed, the result is cached, so that the regular expression is executed only once. The cache is very simple. When the cache is full, is it just discarded and the caching starts from the beginning.
Setting the cache size may affect the performance of tntnet a little. It is settable here. The default size is 8192 entries.
## Example
MaxUrlMapCache 256
# MimeDb
## Syntax
MimeDb file
## Description
The static@tntnet component, which sends files from the file system, uses the specified file to look up the content type depending on the file extension. This is by default /etc/mime.types.
## Example
MimeDb /usr/local/etc/mime.types
# MinCompressSize
## Syntax
MinCompressSize number
## Description
Http-compression for replies smaller than this are not compressed at all. The default value for this is 1024.
## Example
MinCompressSize 1024
# MinThreads
## Syntax
MinThreads number
## Description
Tntnet uses a dynamic pool of worker-threads, which wait for incoming requests. MinThreads specifies, how many worker threads there have to be. This defaults to 5.
## Example
MinThreads 10
# MaxThreads
## Syntax
MaxThreads number
## Description
Tntnet uses a dynamic pool of worker-threads, which wait for incoming requests. MaxThreads limits the number of threads. The default is 10.
## Example
MaxThreads 20
# NoCloseStdout
## Syntax
NoCloseStdout 0|1
## Description
If Daemon is set to 1, tntnet closes standard-in-, standard-out- and standard-error-channels, unless NoCloseStdout is set to 1.
## Example
NoCloseStdout 1
# NoMonitor
## Syntax
NoMonitor 0|1
## Description
On startup, if Daemon is set to 1, tntnet does a second fork. The parent keeps waiting for the child and the child does the work. If tntnet crashes, what might happen, when a webapplication is buggy, the worker-process is restarted. This can be switched off by setting NoMonitor to 0.
## Example
NoMonitor 0
# PidFile
## Syntax
PidFile filename
## Description
When run in daemon-mode, tntnet writes the process-id of the monitor-process to filename. When the monitor-process is deactivated, the pid of the worker-process is written. This ensures, that sending a sigkill to the the stored process-id stops tntnet.
## Example
PidFile /var/run/tntnet.pid
# PropertyFile
## Syntax
PropertyFile filename
## Description
This directive specifies the property-file, where logging is configured. The content of the property-file is dependend of the underlying logging-library.
## Example
PropertyFile /etc/tntnet/tntnet.property
# QueueSize
## Syntax
QueueSize number
## Description
Tntnet has a request-queue, where new requests wait for service. This sets a maximum size of this queue, after wich new requests are not accepted. The default value is 100.
## Example
QueueSize 50
# SessionTimeouot
## Syntax
SessionTimeout seconds
## Description
This sets the number of seconds without requests after which a sesssion is erased. The default value is 300 seconds.
## Example
SessionTimeout 600
# SocketReadTimeout
## Syntax
SocketReadTimeout milliseconds
## Description
A worker-thread waits for some milliseconds on incoming data. If there is no data, the job is put into a queue and another thread waits with poll(2) on incoming data on multiple sockets. The workerthreads are freed and they can respond to other requests quickly. The default value is 200 milliseconds, which is good for normal operation. A value of 0 results in non-blocking read.
If timeout is reached, this does not mean, that the socket is closed.
A small timeout reduces contextswitches on slow connections.
## Example
SocketReadTimeout 0

# SocketWriteTimeout
## Syntax
SocketWriteTimeout milliseconds
## Description
This defines the time, how long the workerthreads wait on write. If the timeout is exceeded, the socket is closed and the browser might not get all data. The default value is 10000 milliseconds.
## Example
SocketWriteTimeout 20000
# SslListen
## Syntax
SslListen ip [port[ssl-certificate-file [ssl-key-file]]]
## Description
Specifies, on which ip and port tntnet waits for incoming ssl-connections. Optionally a certificate- and key-file can be passed.
## Example
SslListen 192.168.0.1 8443
Waits on the specified address and port on incoming ssl-connections. The server is reachable with https://192.168.0.1:8443/
# ThreadStartDelay
## Syntax
ThreadStartDelay ms
## Description
## Example
ThreadStartDelay 1000
# User
## Syntax
User username
## Description
## Example
User www-data
# VMapUrl
## Syntax
VMapUrl host url component-identifier [ path-info { additional-arguments } ]
## Description
This is like MapUrl, but is specific for the virtual host.
This rule matches only if the host and the url matches against the specified
values. Both are regular-expressions, so one rule can also match multiple hosts.
## Example
# maps request for the host www1.tntnet.org to application1
VMapUrl www1.tntnet.org /([^/.]+)	$1@application1
# maps request for the host www2.tntnet.org to application2
VMapUrl www2.tntnet.org /([^/.]+)	$1@application2
# maps all calls to port 8000 to myapp
VMapUrl .*:8000 /([^/.]+)	$1@myapp